|  |  | CPW 0604 CNC Production Welder |
| --- | --- | --- |
| Technical Data |
| Working range | 23.6” x 16.53” x 4.7” (600 x 420 x 120 mm) (maximum working range for 1 welding head) |
| T-slot work plate | 31.5” x 19.3” (800 x 490 mm) |
| Welding range | #4 to 5/16'', dia. #4 to 5/16'' (M3 to M8, dia. 3 to 8 mm); dia. 3/8'' to 1/2'' (dia. 10 to 12.7 mm) only possible with modification |
| Stud length | 0.31'' to 1.57'' (8 to 40 mm) other lengths on request |
| Welding capacity | Up to 30 studs/min (depending on stud welding unit, stud type and positioning of stud) |
| Traverse speed | 82’/min (25 m/min) X-Y, 65.6’/min (20 m/min) Z |
| Stud feeding | Automatic stud feeding (up to 3 different stud length per welding head) (not included in delivery) |
| Positioning accuracy of welded stud | ± 0.008" (± 0.2 mm) |
| Positioning and repeat accuracy | ± 0.002'' (± 0.05 mm) |
| Stud welding head | KAH 412 Optional: KAH 412 LA (mechanical length compensation - gap) (not included in delivery) |
| Max. number of stud welding heads | 1 |
| Connections | Electrical: 480 V, 16 A, 60 Hz (other voltages and frequencies on request) Pneumatic: 6 bar min./10 bar max./inner hose dia. 6 mm |
| Motor-driven Z-axis | Z = 0 to 4.7'' (0 to 120 mm) free programmable because of servo drive technology |
| Controller | High performance PLC IEC 61131-3 |
| Display | 9“ Touchscreen |
| Keyboard | Touch |
| Dimension L x W x H | 63” x 37.4” x 74.8” (1600 x 950 x 1900 mm) |
| Weight | Approx. 1,411 lbs (640 kg) |
| Order No. | 88-21-381 |
| General Information |
| Process variants Tip ignition (CD) Drawn arc welding (ARC) Short cycle drawn arc welding (SC) |
| Equipment User friendly and self-explanatory menu navigation Very high welding capacity through intelligent program architecture Multilingualism Possibility of individually set zero points Quick change system for stud welding heads Fast and easy programming through user guided program editor USB flash drive 4 GB Rewelding function without continuation of the program after stop Flexible connectors for ground clamps Integrated display of cycle time and work piece counter |
| Structure Machine base frame Machine protection cover Solid work table Positioning of work pieces Fully automatic welding program Storage: 1000 programs with 200 lines each Anti wear protection on work plate Integrated zero-point-stop Display for error indications High precision ball screw system Ring initiator High positioning accuracy of the unit through rugged design and linear guidance with ball bearings Welding cable guidance inside the energy chains Continuous documentation of mechanical and electrical components |
| Options Stud welding heads with length compensation (mechanical or electronic) Work piece fixtures Flexible fixture concept Single stud feeding PBZ Pneumatic feeding switch point Pneumatic clamp Work piece down holder Spray regulator unit Shielding gas module |
| Advantages |
| Features High welding capacity High traverse speed Advanced technology High quality product Cost savings Reliable Very short change-over time Free programmable stroke of Z-axis (0 to 120 mm) |
| Suitable stud welding units CDMi 2402, CDMi 3202, ARC 800, ARC 1550, IT 1002, IT 90 |
| Issue 09/16 (Technical data may change) |