|  |  | MPW CNC Multi Production Welder |
| --- | --- | --- |
| Technical Data |
| Working range | 49.21'' x 41.34'' (1 250 x 1 050 mm) MPW 1010; 49.21'' x 88.58'' (1 250 x 2 250 mm) MPW 2010 (maximum working range for up to 3 welding heads) |
| Welding range | #4 to 5/16'', dia. #4 to 5/16'' (M3 to M8, dia. 3 to 8 mm); dia. 3/8'' to 1/2'' (dia. 10 to 12.7 mm) only possible with modification |
| Stud length | 0.31'' to 1.57'' (8 to 40 mm) other lengths on request |
| Welding capacity | Up to 30 studs/min (depending on stud welding unit, stud type and positioning of stud) |
| Traverse speed | Up to 157.48'/min (48 m/min) |
| Stud feeding | Automatic stud feeding (up to 3 different stud length per welding head) (not included in delivery) |
| Positioning accuracy of welded stud | ± 0.008" (± 0.2 mm) for steel and ± 0.008" (± 0.2 mm) for aluminum (depending on work piece and stud geometry) |
| Positioning and repeat accuracy | ± 0.002'' (± 0.05 mm) |
| Stud welding head | KAH 412 Optional: KAH 412 LA (mechanical length compensation - gap) (not included in delivery) |
| Max. number of stud welding heads | 4 (up to 3 stud lengths per welding head possible) |
| Connections | Electrical: 400 V, 32 A, 50 Hz Pneumatic: 6 bar min./10 bar max./inner hose dia. 1/4'' (dia. 6 mm) |
| Motor-driven Z-axis | Z = 0 to 7.87'' (0 to 200 mm) free programmable because of servo drive technology |
| Dimension L x W x H | 94.49'' x 106.30'' x 122.05'' (2 400 x 2 700 x 3 100 mm) MPW 1010; 141.73'' x 106.30'' x 122.05'' (3 600 x 2 700 x 3 100 mm) MPW 2010; |
| Dimension L x W x H with machine protection cover | 149.61” x 187.01” x 118.11” (3 800 x 4 750 x 3 000 mm) MPW 1010 |
| Dimension L x W x H with protective light grid | 157.48” x 145.67” x 122.05” (4 000 x 3 700 x 3 100 mm) MPW 1010 208.66” x 145.67” x 122.05” (5 300 x 3 700 x 3 100 mm) MPW 2010 |
| Order No. | According to project |
| General Information |
| Application Basic milling operations (optional) Milling of the welding position for removing anodising or zinc layers prior to welding Removal of spatter around the welding stud with crown cutter after welding |
| Process variants Tip ignition (CD) Drawn arc welding (ARC) Short cycle drawn arc welding (SC) |

Equipment Graphic user interface (Windows 7) Easy menu navigation Continuous path control CNC-programming according to DIN 66025 Very high welding capacity through intelligent program architecture Multilingualism Free zero point Quick change system for stud welding heads Fast and easy programming through user guided program editor Industrial-PC-controlled Hard disc with 60 GB memory capacity Rewelding function and continuation of the program after stop Flexible connectors for ground clamps Very short set-up time (a.e. automatic calibration of Z axes) Integrated display of cycle time and work piece counter Network connection

Structure High precision ball screw system High positioning accuracy of the unit through rugged design and linear guidance with ball bearings Clear welding cable guidance inside the energy chains Machine accessibility from all 4 sides through a side-mounted switchboard cabinet behind the Y working range Operating panel Detailed documentation of mechanical and electrical components

Options HBS-CAD with DXF-files converter and network interface card for external programming Flexible fixture concept Machine protection cover (only for MPW 1010) Customer specific handling systems Single stud feeding PBZ Pneumatic clamp Workpiece downholder Spray regulator unit Shuttle table (only for MPW 1010) Swivel stop HBS Code Reader HBS Dual Milling Unit HBS Adjustment set for welding head position

Advantages

Features High performance servo motors (Vmax = 48 m/min) Up to 8 servo axes Very short change-over time Free programmable stroke Z-axis (0 to 200 mm)

Safety Safety equipment according to latest and accident prevention regulations light barrier with fence (safety class 4)

Welding High welding rates Fully automatic program sequence for welding

Suitable stud welding units CDMi 2402, CDMi 3202, IT 1002, IT 90

Issue 09/17 (Technical data may change)